Project «LowBlow» EEPROM structure
General
We have 128 bytes of EEPROM, starting from address 0.

EEPROM structure is next:
Addresses	Values
0x00 - 0x01	Base temperature, uint16_t
0x02	Base RPMs, uint8_t
0x03	Steps table, 125 steps, each step is uint8_t.
...
0x7F

Base temperature
Base temperature stored as uint16_t, i.e. least significant byte at 0x00 and most significant byte at 0x01. Any value possible.

Base RPMs
In MCU firmware there is next values for RPMs:
Value	Meaning
0x00	Cooler Off
0x01	Minimal RPMs
0x100	Maximal RPMs

We are storing Base RPMs as uint8_t, and it is meaningless to have «Cooler Off» as base RPMs. So, MCU_{BaseRPMs}=EEPROM[ 0x02 ] + 1 .

Steps
Each step is a byte, divided into two parts:
7	6	5	4	3	2	1	0
Delta RPMs				Delta T

Delta T can not be 0, so actual temperature increase is Delta T + 1, thus [1-16]. Delta RPMs can be zero, so it [0-15].